## Slide 1
Background:
Reliability and security of FPGA devices are now much more concerned issues due to counterfeiting device and Hardware Trojan (HT)
Result and Future Work
Proposed System to Detect Counterfeiting device
Ahmed Foisal, Mian Riaz-ul-Haque, Islam Syful, and Michihiro Shintani
Dependable System laboratory, Graduate School of Information Science, Nara Institute of Science and Technology (NAIST)
FPGA Reliability and Security
Objective:
Development a system to detect counterfeiting devices and HT for reducing probability of catastrophic consequences on safety critical applications such as defense, aerospace, medical, nuclear plant etc.
CICP 2017 || Dependable System Laboratory, School of Information Science , Nara Institute of Science and Technology
Currently we have focused only on the FPGA reliability
As the future work, we can extend our current work for security issue more elaborately, specially for Hardware Trojan detection.
Future work:
Manufacturer
Retailer
User
Counterfeit
Attacker
✔
✔
UNRELIABLE
Device under
analysis with RO
Suspicious FPGA
Ring Oscillator (RO)
Enable
1
2
3
4
5
6
7
Out
Enable
Out
time
Host PC
UART Module
FPGA
Test
command
Measured
data
Frequencies of
ROs on FPGA
Frequency is utilized
as a fingerprint of
each device
Display on monitor
(1)database
(3)identification
Measure
User
Manufacturer
T(p1,p2,…,pi)
ID=1
V1(p1,p2,…,pi)
ID=n
Vn(p1,p2,…,pi)
…
(2)inquiry
Genuine?
Genuine or not
ID=2
V2(p1,p2,…,pi)
Identification through machine learning
- Learn f based on training data set from the database
- Then, the device ID of new devices are estimated using f
= f
x1
xn
…
P(1,1), p(1,2),…, p(1,i)
P(n,1), p(n,2),…, p(n,i)
…
system
X1: device ID=1
P(1,1),p(1,2),…,p(1,i)
:Feature vector
frequency
Using ring oscillator, frequency is measured in different row and column position inside the FPGA.
Fingerprint of genuine and counterfeited FPGA looks different shape due to spatial process variations.
Used BASYS-3 FPGA board and ZYBO FPGA board of Xilinx Corp. for training and testing proposed technique.
Finally using Machine Learning technique classify the counterfeited FPGA from genuine FPGA.
Detect Counterfeited FPGA
Detect New FPGA